## Slide 1: Learn CIA and Parser

## Slide 2: Design parameters for last year’s class

## Slide 3: The New CIA initial thoughts
Use aspects of ARM
  Load Store
  32 bit addressing
  32 bit instruction/opcodes
8 registers supported for destination and source
  9 bits for register related items in opcode (3 destination, 3 source 1, 3 source 2)
32 bit data support, but…
  16 bit immediate in instructions max
Don’t go crazy with addressing modes
  From register, register with offset
  Offsets share data field
6 bits for instruction type and function
Must support minimum set of flags: Carry (unsigned overflow), Negative, Zero, V (Signed Overflow)
  Pretty much what is need to support branches and errors in the ALU.
Leaves 1 extra bit if needed for something else like extending instructions to 7 bits…

## Slide 4: New instructions brainstorm…
MOV and MOVT (MOV32 = MOV followed by MOVT)
NOP
LOAD
STOR
ADD
SUB
CMP
AND, OR, XOR, NOT
JMP
B, B., BNEVER
HALT
LSL and LSR
CLR

## Slide 5: Class Processor instruction list Data move movement
NOP
Load IMM to REGx
  MOVZ (Move Immediate)
  MOVN
Load
  LDR
Store
  STR
Branch Conditional
  B.cond
Branch Unconditional Register
  BR
Branch Unconditional Immediate
  B

## Slide 6: Class Instruction set ALU
ADDS
SUBS
BFM
CCMN
AND
ORR
EOR
EON

## Slide 7: Fall 2022 Task
As a group, decide on a simple problem(s) to solve using the CIA
  Must use every instruction at least once
  We will use this to help check the SCC
  Can be more than one “program”.
  Ideas due by End of class Wed.
Using the simple problems
  Each team will write code using the CIA for the problems
  Design using named CIA instruction in assembly format
  Compile to opcode using the parser (any bugs identified and fixed gets a bounty)
  Check and confirm your results
  Due two weeks
Each group will score/check another group for completeness and accuracy
  Due three weeks.